## Slide 1
☄ METEOR — Optimization Log
Every improvement started as a measured failure
12 rounds · 4 new task heads · temporal fusion — in one week
Dan Umeda — TIER IV, Inc. · built on CoMET / Co-MLOps

## Slide 2
The improvement journey
each round diagnosed one weakness and fixed it, warm-starting the next
Round | Model | Improvement | Key metric | Result
r5 | v17 | + 10-class 2D detection | BEV mIoU | 0.286
r6 | v16 | lane / ego-vehicle GT fix | 2D-seg lane IoU | 0.371
r7 | v18 | + E2E driving head | traj ADE | 0.95 m
r8 | v19 | head capacity re-balance + KMAX 96 | BEV mIoU / 2D-seg | 0.293 / 0.450
r9 | v20 | + occupancy, E2E curvature weighting | curve ADE | 2.31 → 0.72 m
r10 | v20 | small-object / near-VRU / side-cam weights | 2D-seg lane | 0.548
r11 | v21 | + one-shot agent trajectory forecast | agent ADE | 2.17 m
r12 | v22 | temporal BEV fusion (streaming, TRT-safe) | curve ADE (ep0) | 2.28 → 1.91 m
warm-started throughout — a class-count change retrains only the affected head; nothing restarts from scratch

## Slide 3
① Head capacity: parameters at low resolution, compute at high
symptom — 2D heads were 'high FLOPs, low params': the worst trade-off
PROBLEM
3×3 convs at stride-4 (full res)
weak 2D seg (mIoU 0.362) and
small classes never detected
FIX
encoder–decoder seg head
(heavy channels at s8/s16)
3-scale YOLO-style detection
1×1 laterals only at s4
EFFECT
2D-seg mIoU 0.362 → 0.450
pole IoU 0.251 → 0.449
+18× params for +2× FLOPs
model +37% params / +10% FLOPs
• Design rule: put channels where pixels are cheap (s8/s16), touch full resolution only through 1×1
• Traffic lights, distant signs and cones — previously silent classes — began firing

## Slide 4
② Small objects were silently deleted by the GT pipeline
symptom — cones / traffic lights / distant unknowns almost never detected
• Root cause 1 — box budget truncation
– per-camera cap of 32, area-sorted → dropped 29% of annotations in crowded scenes (all small)
– fix: KMAX 32 → 96 + per-class positive weights (obstacle ×3, two-wheeler/light ×2)
• Root cause 2 — thin classes vanish on downsample
– a lane line is ~0.3 px wide at stride-4 GT; nearest-neighbour resize deletes it
– fix: coverage-based rasterisation (cell = thin class if >12% covered) → +49% lane pixels
• Effect: 2D-seg lane IoU 0.371 → 0.548; obstacle / light / sign classes detected in demos

## Slide 5
③ The E2E head learned to 'always go straight'
symptom — planning looked fine on average, failed on every curve
DIAGNOSIS
83% of frames are near-straight
longitudinal targets ~18× larger
than lateral → plain L1 ignores
steering signal
aggregate ADE 0.86 m HID it
FIX
lateral error weight ×4
per-sample curve weight
1 + |lat@3s| / 1.5 (up to ×5)
new metric: curve-only ADEc
reported every epoch
EFFECT
curve ADE 2.31 m (start)
→ 1.07 m (1 round)
→ 0.72 m (2 rounds)
straight frames unchanged
(0.62 m)
• Lesson: measure per-condition. The failure was invisible until we conditioned the metric on curvature.

## Slide 6
④ Ground-truth bugs found by watching the demos
• Scene-tail speed bug
– instantaneous v0 left at 0 past the 3 s-future cutoff → model, conditioned on a bogus 0, predicted
– 'HOLD' at 80 km/h. Fix: write v0/steer/accel for every frame; only trajectory carries a validity mask
• Ego-vehicle unsupervised
– the hood was 'ignore' → free-running noise. Fix: supervise ego as background → clean hood region
• Best-checkpoint criterion
– 'best' was BEV-mIoU only → a pre-curve-fix epoch got inherited. Fix: composite score (mIoU − 0.01·ADEc)
• Occupancy hallucination
– coarse 1.7 m ray-carving left above-road voxels 'unknown' → confident phantom structure.
– Fix: 0.4 m dense carving + per-class confidence gates in visualisation

## Slide 7
⑤ Two new tasks added at negligible cost
3D semantic occupancy (v20)
10-class voxels, 16 × 200 × 200 @ 0.4 m
GT: multi-sweep labeled LiDAR (sampled from
cached 2D-seg, no RLE decode — 690→45 s/scene)
dynamic-object de-smearing (±1 frame only)
0.4 m ray-carved free space
cost: +0.70 M params / +55 GFLOPs (2%)
One-shot agent forecasting (v21)
per-detection future offsets, 6 × 0.5 s
constant cost in the number of agents
(dense regression on the detection grid)
GT: instance_token tracks → current ego frame
agent ADE 2.17 m (single frame)
cost: +0.002 M params (a 1×1 conv)
• Both share the existing BEV feature and detection stem — 'adding a task' became a head, not a network.

## Slide 8
⑥ Temporal fusion — velocity becomes observable
single-frame perception cannot see motion; a streaming BEV can — without breaking TensorRT
• Previous frame's raw BEV is ego-motion-warped into the current frame (affine_grid + grid_sample) and
– residual-fused with the current BEV — TensorRT-safe operators only, no RNN
• Deployment: prev-BEV + warp matrix are graph INPUTS, current BEV an extra OUTPUT → static feed-forward
– cost: +0.19 M params, +5% step time (measured); ONNX/TensorRT-exportable as-is
• Early effect (1 epoch): curve ADE 2.28 → 1.91 m; agent forecasting expected to gain most from motion cues
– Debugging note: a no_grad forward inside an autocast region cached detached fp16 weights and
– all backbone gradients under DDP — diagnosed with TORCH_DISTRIBUTED_DEBUG on a 2-GPU mini-run

## Slide 9
Quantitative summary
held-out recording · every gain without a single human label
Metric | Before | After | Driver
BEV lane mIoU | 0.283 | 0.293 | capacity + data
2D-seg mIoU (21 cls) | 0.362 | 0.458 | ED head + KMAX 96
2D-seg lane IoU | 0.371 | 0.548 | coverage rasterise + weights
2D-seg pole IoU | 0.251 | 0.449 | 3-scale detection
E2E curve ADE | 2.31 m | 0.72 m | curvature weighting
E2E curve ADE (temporal, ep0) | 2.28 m | 1.91 m | temporal fusion
Agent forecast ADE | — | 2.15 m | new task (v21)
Model size | 26.8 M | 38.5 M | 8 tasks + temporal

## Slide 10
Principles that generalised
• Measure per-condition — aggregates hide the failures that matter (curves, ranges, rare classes)
• Add the diagnostic metric with the fix — ADEc, per-range occupancy IoU, per-class detection counts
• Deployment constraints are design inputs — TensorRT-safe ops shaped the temporal fusion, not the reverse
• Capacity has a shape — parameters at low resolution, compute at high resolution
• Watch the output, not just the loss — the scene-tail and ego-vehicle bugs were found in demo videos
• Warm-start everything — 12 rounds, 4 new heads, temporal fusion, and never a cold restart

## Slide 11
From one task to eight — plus time
a new task went from 'a labeling campaign' to 'a head and a GPU-day'
github.com/tier4/METEOR
Labels by machines. Code by Claude Fable 5. Direction by humans.